## Slide 1
SANITATION SYSTEMS AND
ENVIRONMENTAL PROTECTION ACTIVITIES
IN ISTANBUL CITY
Dursun Ali ÇODUR
ISKI General Director
16.03.2006

## Slide 3
The Bosphorus

## Slide 4
Rumeli Castle

## Slide 5: Istanbul Water and Wastewater Administration ISKI
ISKI is the public operator for the water and wastewater services in Istanbul Metropolitan Area.
Provide services for population of 12 million.
Total area served 6,504 km2.
Provides water and wastewater services for 246 municipalty.
3.7 million contractual customers.
Total length of water network is 12.698 km.
Total length of sewage system is 9.736 km.
Average of daily water supply is 2.000.000 m3/day.
Average of daily treated wastewater is 1.910.000 m3/day.
Number of staff is 6.191
Notes: Before the 18th century all the waste water was thrown on the street, polluting the soil and the aquifer and above all the wells because of non watertight septic tanks. Several cholera epidemics occurred all along the 18th century killing 18 400 people in 1832 in Paris. The building of a fresh water network increases the consumption of water from 4 l/d to 120 l/d.
In 1807 a public water and sanitation service is created, Belgrand put in place the Principe that each house should be connected to a pipe to evacuate the water downstream of Paris. That Principe has a big impact on the Seine River.

## Slide 6
Infrastructure and sanitation problems due to fast growing population and rapid urban development.
Delayed infrastructure investments because of wrong planning, wrong selection of the priorities and corruptive practices.
Incompleted wastewater collection and disposal systems. Nearly all wastewater of Istanbul was discharged into sea, rivers and water resources.
Insufficient wastewater treatment capacity. Only about 10% of discharged wastewater treated.
Sanitation Services of Istanbul in early 1990’s

## Slide 7
Sea water pollution and unpleasant odours. The sea water ecosystem specially in Golden Horn was seriously damaged as a result of wastewater discharges.
Closing down of beaches and “Forbidden to Swim” signboards.
Pollution threat of drinking water resources and catchment basins.
The sea water transportation in the Golden Horn was totaly abondoned.
The tourism activities was effected badly. Consequently loss of jobs and economy.
Sanitation Services of Istanbul in early 1990’s

## Slide 8: Investments for Sanitation Services following the year 1994
Construction of 9 Wastewater Treatment Plants. (4 Biological and 5 Primary Treatment)
Construction of 17 wastewater pumping stations.
Construction of 54 km tunnel interceptor systems.
Construction of 762 km interceptor and collectors systems.
16 km marine outfall.
Sea Water Quality Monitoring Studies conducted in cooperation with several Universities.
Wastewater treatment and disposal strategies based on the water quality studies.
Pollution levels of the sea water is measured at 45 stations for 40 different parameters.
Advanced technologies are used in wastewater operational services, robot technology and pipe-jacking.
Notes: Before the 18th century all the waste water was thrown on the street, polluting the soil and the aquifer and above all the wells because of non watertight septic tanks. Several cholera epidemics occurred all along the 18th century killing 18 400 people in 1832 in Paris. The building of a fresh water network increases the consumption of water from 4 l/d to 120 l/d.
In 1807 a public water and sanitation service is created, Belgrand put in place the Principe that each house should be connected to a pipe to evacuate the water downstream of Paris. That Principe has a big impact on the Seine River.

## Slide 9
Location of Wastewater Treatment Plants and interceptors
Tuzla
Kadıköy
Paşaköy
Üsküdar
Terkos
Küçüksu
Baltalimanı
Yenikapı
Ataköy
K.Çekmece
B.Çekmece
Existing
Under Construction
Planned
Paşabahçe
Ataköy
Ambarlı
Bahçeşehir
Çanta
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10
The percentage of the treated wastewater has risen from 10% in 1994 up to 85 % in 2005.
Water resources are saved by applying advanced treatment techniques.
Significant improvements in coastal water quality and odour problems.
138 km out of 284 km of Istanbul coast are available to swim by blue flag criterias.
Major Environmental gains and improvments

## Slide 11
With the improvements in sea water quality, Istanbul seasides once again attracts tourism and sea sports.
Means of beach holiday for people with less income without travelling.
Major Environmental gains and improvments

## Slide 12: Financials aspects
Water consumers pay for all water supply and sanitation systems.
The water tarifs are about;
House-1 (1-30 m3) : 1,12 $/m3
  House-2 (31 and plus) : 2,24 $/m3
  Commercial : 2,24 $/m3
Total investment of 3 billion $ (US) in sanitation systems since 1994.
The total budget of 2006 is about 1,282 billion $ (US).
The investment budget of 2006 is about 778 million $ (US).
Total investment on water, wastewater and stormwater projects up to 2032 is estimated 10 billion $ (US).
Notes: Before the 18th century all the waste water was thrown on the street, polluting the soil and the aquifer and above all the wells because of non watertight septic tanks. Several cholera epidemics occurred all along the 18th century killing 18 400 people in 1832 in Paris. The building of a fresh water network increases the consumption of water from 4 l/d to 120 l/d.
In 1807 a public water and sanitation service is created, Belgrand put in place the Principe that each house should be connected to a pipe to evacuate the water downstream of Paris. That Principe has a big impact on the Seine River.

## Slide 13
A case study:
The Golden Horn
Environmental Protection
Project

## Slide 14
The Golden Horn before pollution

## Slide 15
In past years due to wrong city planning, Golden Horn was turn into an industrial region.
When came to 1985, about 700 industry places and over 2000 office were established already.
The Golden Horn polluted by industries
Notes: <number>
<footer>
<header>
<date/time>

## Slide 16
It was impossible to approach the Golden Horn because of pollution and unpleasant odors.
The Golden Horn Environmental Pollution
Notes: <number>
<footer>
<header>
<date/time>

## Slide 17
The Golden Horn Environmental Pollution
Golden Horn was begun to pollute in a short period because of
industrialization.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 18
Haliç
Wastewater formerly discharged direct into the Golden Horn is collected and transferred to treatment plants.
The sludge that had accumulated in the course of time was dredged and collected in a convenient place.
Rehabilitation of the Golden Horn and its environment.
Works done to
rescue Golden Horn

## Slide 19
Cleaning Works of Golden Horn
Notes: <number>
<footer>
<header>
<date/time>

## Slide 20
Cleaning Works of Golden Horn
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21
Filling area of disposed sludge
Recreation of the filling area

## Slide 22
The Golden Horn Before and After Rehabilitation
Notes: <number>
<footer>
<header>
<date/time>

## Slide 23
As the result of the total Investment of 653 million $, today;
33 species of fish are living in Golden Horn and the extinct
seahorse also live in Golden Horn.
Sea transport, which had stopped 20 years before, has restarted.
International Boat Races are organized in the Golden Horn
The Golden Horn
Environment Protection Project was awarded First Prize in 2002
“Metropolis Award”
Notes: <number>
<footer>
<header>
<date/time>

## Slide 24
www.iski.gov.tr
thank you..
Notes: <number>
<footer>
<header>
<date/time>